## Slide 1: AZARUL FAHMIN BIN AB HAMID SUNGAI PETANI,KEDAH 19 AUGUST 1992 EDUCATION: DIPLOMA IN MECHATRONIC ENG. ,2013 BACHELOR OF SCIENCE MECHATRONIC ENG. , 2017 PAPER: CONNECTED CAR: ENGINE DIAGNOSTIC WITH INTERNET OF THINGS(IoT) EXPERIENCE: PROJECT FREELANCE, 2010-2016 FREELANCE TRAINER, 2012-2016 TRAINING MANAGER NADI ELECZONE, 2017 PROJECT AND AWARD: PINTAR (Penanti innovation talent recreation centre) SCIENCE ON WHEEL(NORTH REGION) EDUCATION INNOVATION AWARD, YPJ
NADI ELECZONE SOLUTIONS
SA0311162-X
CONTACT NUMBER: 013 4094377

## Slide 2: MUHAMMAD AIDIL FAIZ BIN ISMAIL KEPALA BATAS, PENANG 25 MARCH 1993 EDUCATION: DIPLOMA IN MICROELECTRONIC ENG. ,2013 BACHELOR OF ELECTRONIC ENG. , 2017 PAPER: e-Padi: An IoT Based Paddy Productivity Monitoring System EXPERIENCE: PROJECT FREELANCE, 2014-2017 FREELANCE TRAINER, 2015-2017 PROJECT AND AWARD: Gold Medal E reka UniMAP 2017 (E padi) Gold Medal I-Envex 2016 (IoT Clean room monitoring) SCIENCE ON WHEEL(NORTH REGION)
NADI ELECZONE SOLUTIONS
SA0311162-X
CONTACT NUMBER: 013 4094377

## Slide 3: Internet of Things (IoT) Advance Training

## Slide 4
Download the software here!!
arduino
Installing Arduino IDE
Go to website url https://www.arduino.cc/en/Main/Software and downlad Arduino IDE software. Take the windows installer or windows zip.
. If you are taking the windows zip it’s mean you choose non admin install that don’t need t be install. You just have t extract the file
1
2

## Slide 5
This process will extract and Install the file that will be use in Arduino software(IDE)
Select Installation Folder (We suggest to use- Default)
Choose component to Install
Download/ Copy Arduino Software (IDE)
Step 1
Step 2
Step 3
Step 4
Installing Arduino IDE

## Slide 6
NodeMCU Board Library Setup
Go to File  Preferences copy this json url and paste http://arduino.esp8266.com/stable/package_esp8266com_index.json into Additional Board Manager URLS: then click OK
Go to ToolsBoardsBoard Manager click Board Manager and then wait for a few minute until nodeMcu library link appear then click Install at esp8266 by ESP8266 community
1
2

## Slide 7
What is IoT???
Internet of Things (IoT), is one of popular word today, but most of person still don’t understand about IoT. For now we are in 4th industry revolution that will use IoT as one of technology component as a physical communication medium. IoT is a technology to communicate data(sensor, decision and etc) between any electronic devices.
Why IoT???
There are many communication method that can be make in state of wireless but why insist to use IoT as a medium of communication.

## Slide 12
Get to know NodeMCU
(USB Port and GPIO)
1
Function of USB Port
To see NodeMCU Board status
Use to upload compiled code from Arduino IDE into NodeMCU board.

## Slide 13
Using Arduino IDE
What the important thing you need to know when the first time you are using arduino?
Here you can see if the NodeMCU board already connected to the computer by looking at the port.
From here you can get many example coding to be use.
Button Verify
Button Upload
1
2
3

## Slide 14
Arduino IDE adding library setup
1
Copy this three library file
2
Paste in C://Program file(x86)/Arduino/libraries

## Slide 15
Lesson 1 : Get to know OUTPUT
1
Connect the LED to NodeMCU board.
D7= pin 13 //folow pin as in GPIO pin out
Every program in Arduino will have one void setup() and one void loop(). Void setup() is for program code that will running once and void loop() is like main program that will continuously running

## Slide 16
Algorithm Syntax that widely used in Arduino programming.
analogRead(pin) (INPUT)
analogWrite(pin,value) (OUTPUT)
digitalRead(pin) (INPUT)
digitalWrite(pin,value) (OUTPUT)
+ꝏ
-ꝏ
1
0

## Slide 17
Lesson 1 : Get to know OUTPUT
2
Write the code in Arduino IDE
After done writing the code click upload . And the led will blink continuously with 1 second(delay(1000); = 1000 milisec delay).

## Slide 18
Lesson 2 : Trying DHT11
1
DHT11
+
OUT
-
3.3V
D1
GND
Sensor pinout

## Slide 19
Lesson 2 : Trying DHT11
2
Library function caller
Define sensor pinout
Define DHT sensor type
Set Serial Monitor baudrate
Call function to read humidity and temperature value then store it in h and t variable.
Print data to appear in Serial Monitor. Serial.print is for print the value and when it’s come to Serial.println it will go to new line.
Done? Then go open the Serial Monitor with this icon

## Slide 20
Setup Thingspeak
1
2
3
Give a name to your channel and field for each of your sensor data. Scroll to the bottom and click save channel.
Goto https://thingspeak.com/ and signup. You need to validate account by using your email.
Click New Channel

## Slide 21
Setup Thingspeak
Go to Sharing then tick on Share channel view with everyone

## Slide 22
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps
1
2
Save your Channel ID in notepad
Save also this two api key

## Slide 23
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps
HTTP Request
HTTP Response
HTTP Request

## Slide 24
1
POST /update HTTP/1.1
Host: api.thingspeak.com
Connection: close
X-THINGSPEAKAPIKEY: GVJHFB678JHU
Content-Type: application/x-www-form- urlencoded
Content-Length: 20 Data: field1=30&field2=40
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 25
1
2
Open thingspeak_dht22.ino
Change xxx at ssid according to your Wi-Fi name
Change xxx at password according to your Wi-Fi password Change xxx at writeAPIKey according your api key in thingspeak
After done. Please take a look at thinspeak channel to see your incoming data.
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 26
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps
1
2
Open http://ai2.appinventor.mit.edu/ and signup
Start new project and give a name to your apps

## Slide 27
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 28
To change your properties for your component. You need to edit it here.
All the component that you take from pallete will be shown here.
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 29
If you want to delete your block you can dump in this bin
Here is all of syntax that you will use in programming the android apps. The block that you drag form here can be compare by the colour of the block
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 30
Drag 4 Lable into your screeen
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 31
You need to change text for each label at here.
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 32
Put clock into screen that you can get from Sensors
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 33
Pelajaran 3 : Hantar data dari NodeMCU ke Android apps melalui cloud
Drag two Web form Connectivity into screen

## Slide 34
Go to the block then drag all of this component into the coding space
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 35
Put https://api.thingspeak.com/channels/channel id anda /fields/ nombor field /last? Into text field
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 36
Put Clock1.Timer and call web get
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 37
Drag web1 and web2 got text
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 38
Go to the build and click on App(save .apk to my computer). Then install it in your phone
Lesson 3 : Sending data from NodeMCU to the cloud then mobile apps

## Slide 39
Lesson 4 : Send data from android smart phone to NodeMCU through cloud
1
Put the LED at D7
2
Open thingspeak_controlled.ino

## Slide 40
Change xxx at ssid according to your Wi-Fi name
Change xxx at password according to your Wi-Fi password
Change xxx at myReadAPIKey according to your read api key Change xxx at myChannelNumber according to the channel number
Create another Thingspeak channel
that will used in this lesson
Lesson 4 : Send data from android smart phone to NodeMCU through cloud

## Slide 41
Drag 2 button into screen1
Lesson 4 : Send data from android smart phone to NodeMCU through cloud

## Slide 42
Change the button text into
ON and OFF
Lesson 4 : Send data from android smart phone to NodeMCU through cloud

## Slide 43
Drag 2 web into screen
Lesson 4 : Send data from android smart phone to NodeMCU through cloud

## Slide 44
Algorithm at the block part
Lesson 4 : Send data from android smart phone to NodeMCU through cloud

## Slide 45
https://api.thingspeak.com/update?api_key=write api key &field anda =data
Lesson 4 : Send data from android smart phone to NodeMCU through cloud
If(data == 30){
//ON LED } else //OFF LED
DONE! Build The Apps

## Slide 46
Lesson 5: Combine the lesson 4 and 5
1
Put the LED into D7 and
Combine with DHT sensor
2
Open file thingspeak_combine.ino

## Slide 47
Build your own android apps
Lesson 5: Combine the lesson 4 and 5